## Slide 1
0805 meeting
Notes: [Sources]
- C:\Users\lab508\Desktop\uav_project2\TWO_STAGE_STREAMING_OPTIMIZATION_SUMMARY.md
Deck overview: the two optimization stages and their measured impact.

## Slide 2
階段一：WebRTC + vp8 編碼幾乎消除頻寬壓力
1920×1080 @ 30 FPS 實測：以較高 CPU 成本，換取更適合 Wi-Fi 與遠端監看的傳輸效率。
網路流量降低約 97%
MJPEG
38.55 Mb/s
CPU 64.6% 架構簡單，但 1080p 頻寬高
WebRTC
1.14 Mb/s
CPU 203.9% aiortc/PyAV 軟體編碼仍是代價
2
Notes: [Sources]
- C:\Users\lab508\Desktop\uav_project2\TWO_STAGE_STREAMING_OPTIMIZATION_SUMMARY.md
Stage 1 measurements. WebRTC FPS in the source includes repeated/latest frames and startup catch-up; it is not unique YOLO FPS.

## Slide 3
階段二：VIC 降低輸入端色彩轉換負載
工業相機 YUYV → Jetson VIC（nvvidconv）→ BGRx。色彩轉換改由 SoC 專用硬體執行。
輸入端已硬體加速，但輸出端 WebRTC 軟體編碼仍在 CPU。
9.0%
Final 平均 CPU 降幅
20.4%
Final 幀間隔 P95 改善
3
Notes: [Sources]
- C:\Users\lab508\Desktop\uav_project2\TWO_STAGE_STREAMING_OPTIMIZATION_SUMMARY.md
Stage 2 measurements. Final RSS increased by about 73 MiB; power-saving was not established in the current test order.

## Slide 4
兩階段完成後，瓶頸移到輸出端編碼
已完成
已完成
下一步
① WebRTC
頻寬下降約 97% 適合遠端即時串流
② VIC
Final CPU 降低約 9% 改善幀間隔尾端
③ NVENC H.264
取代 CPU 軟體編碼 並減少 frame copy
4
Notes: [Sources]
- C:\Users\lab508\Desktop\uav_project2\TWO_STAGE_STREAMING_OPTIMIZATION_SUMMARY.md
Synthesis and recommended next engineering priority: Jetson hardware H.264 encoding, startup catch-up fixes, unique-frame timestamps, and fewer copies.